## Slide 1
Henry Swales
THE AQUANTIS OCEAN-CURRENT TURBINE
RENEWABLE ENERGY FROM MARINE CURRENTS
Tow Tank Model Rotor
Rotational Flow Investigation
April 16, 2013
Company Confidential and Proprietary

## Slide 2: Rotational Flow Effects
Primary Drivers:
  Solidity (Chord vs. Radius)
    Match TSR & Cl
  Post-Stall Performance
    Match Hydrofoils & Re#
May be possible to design model rotor to have full-scale solidity, but post-stall performance is very different due to Re# difference and hydrofoil selection.
Chart: AoA (deg)
| -5.95 | -4.96 | -3.96 | -2.94 | -1.92 | -0.87 | 0.1 | 1.21 | 2.1800000000000002 | 3.25 | 4.2699999999999996 | 5.31 | 6.29 | 7.3 | 8.32 | 9.32 | 10.37 | 11.39 | 12.4
Cl SD2030 | -0.391 | -0.319 | -0.25 | -0.166 | -0.072 | 0.006 | 0.105 | 0.267 | 0.438 | 0.557 | 0.659 | 0.736 | 0.804 | 0.879 | 0.958 | 1.015 | 1.06 | 1.08 | 0.999
Cd SD2030 | 0.0523 | 0.0315 | 0.0236 | 0.0187 | 0.0154 | 0.0141 | 0.0148 | 0.0165 | 0.0157 | 0.0146 | 0.0137 | 0.0157 | 0.0193 | 0.0228 | 0.0269 | 0.0334 | 0.0443 | 0.0709 | 0.1818
Chart: AoA (deg)
| -5.95 | -4.96 | -3.96 | -2.94 | -1.92 | -0.87 | 0.1 | 1.21 | 2.1800000000000002 | 3.25 | 4.2699999999999996 | 5.31 | 6.29 | 7.3 | 8.32 | 9.32 | 10.37 | 11.39 | 12.4
SD2030 | -7.4761 | -10.127 | -10.5932 | -8.877 | -4.6753 | 0.42553 | 7.0946 | 16.1818 | 27.8981 | 38.1507 | 48.1022 | 46.879 | 41.658 | 38.5526 | 35.6134 | 30.3892 | 23.9278 | 15.2327 | 5.495

## Slide 3: Test Considerations for Stall Delay
SD2030 Cpmin Range : -1.44 to -6.0 (no stall delay predicted close to rotor tip)
Max tow speed without cavitation (TSR=8, 1m depth): 1.5 m/s
  1/25th Scale Rotor 1.8m Re#: 591,000
  Largest Feasible Rotor 5.0m Re#: 1,623,000
May be worthwhile investigating the value of a test at Re# > 500k utilizing full-scale hydrofoils with BL trips to approximate full-scale performance.
  Large discrepancy in Re# would make accuracy of results highly questionable
  Further development needs to be done to select or design thicker full-scale hydrofoils.
Chart: TSR
| 16.000026664977696 | 15.578973331688811 | 15.157919998399926 | 14.736866665111036 | 14.315813331822152 | 13.894759998533264 | 13.473706665244377 | 13.052653331955488 | 12.631599998666601 | 12.210546665377716 | 11.78949333208883 | 11.368439998799941 | 10.947386665511058 | 10.526333332222169 | 10.105279998933282 | 9.6842266656443936 | 9.2631733323555103 | 8.8421199990666235 | 8.4210666657777349 | 8.0000133324888481 | 7.578959999199963 | 7.1579066659110762 | 6.7368533326221884 | 6.3157999993333007 | 5.8947466660444148 | 5.4736933327555288 | 5.0526399994666411 | 4.6315866661777552 | 4.2105333328888674 | 3.7894799995999815 | 3.3684266663110942 | 2.9473733330222074 | 2.5263199997333206 | 2.1052666664444337 | 1.6842133331555471 | 1.2631599998666603 | 0.84210666657777355
Froude Scaled 45.5m Data | -0.00085431 | -0.00038073 | 9.4725e-05 | 0.00057106 | 0.0010502 | 0.0015269 | 0.0020021 | 0.0024819 | 0.0029642 | 0.0034526 | 0.0039503 | 0.0044619 | 0.0049883 | 0.0055345 | 0.006099 | 0.0066898 | 0.0073091 | 0.007942 | 0.0085736 | 0.0091976 | 0.0097556 | 0.010282 | 0.010784 | 0.011265 | 0.011717 | 0.012115 | 0.012437 | 0.012439 | 0.011937 | 0.010919 | 0.0093017 | 0.0074546 | 0.0056289 | 0.0039889 | 0.0026584 | 0.001648 | 0.00093304
Model Data | -0.001533 | -0.001018 | -0.00052 | -1.7e-05 | 0.00048 | 0.000975 | 0.001471 | 0.001972 | 0.002477 | 0.002993 | 0.003521 | 0.004062 | 0.00462 | 0.005194 | 0.005791 | 0.006409 | 0.007038 | 0.007672 | 0.008312 | 0.008955 | 0.009573 | 0.010188 | 0.010777 | 0.011351 | 0.011873 | 0.012083 | 0.011187 | 0.009496 | 0.00756 | 0.005505 | 0.00444 | 0.003481 | 0.00269 | 0.002064 | 0.001565 | 0.001184 | 0.000914