## Slide 1
Henry Swales
Ole Kils
THE AQUANTIS OCEAN-CURRENT TURBINE
RENEWABLE ENERGY FROM MARINE CURRENTS
1/25th Scale Rotor Preliminary Design
March 19, 2013
Company Confidential and Proprietary

## Slide 2: Conceptual Approach
Re-Design rotor for model scale using hydrofoils designed and tested for tow tank Re# of 168k.
  Maintain Froude scaling of thrust, diameter and rotor speed for dynamic stability tests.
  Minimize performance instabilities due to laminar separation bubbles.

## Slide 3: SD2030 Pressure Distributions
Utilize very thin airfoil with long transition ramp developed for low Re# sail planes and wind turbines.
Minimizes laminar separation bubble thickness.
Airfoil Thickness (%) Camber (%) Cm,c/4
SD2030 8.56 2.23 −0.075

## Slide 4: Clean Airfoil Performance
Despite low Re# design, clean airfoil test data still displays some evidence of a laminar separation bubble at Re# = 100k to 200k.

## Slide 5: Tripped Airfoil Performance
Test data with a leading edge trip shows minimal laminar separation bubble impact on performance at Re#=100,000.
Tripping the boundary layer is also more representative of the fully turbulent flow regime expected at full scale.
  Full Scale Re# @ 0.7R = 10,000,000

## Slide 6: Hydrofoil Comparison
Model: SD2030 @ Re# = 100k
  Design Point: 4deg
  Stall Marin: 8deg
Full Scale: S816 @ Re# = 10M
  Design Point: 5deg
  Stall Margin: 10deg
Chart: AoA (deg)
| -5.95 | -4.96 | -3.96 | -2.94 | -1.92 | -0.87 | 0.1 | 1.21 | 2.1800000000000002 | 3.25 | 4.2699999999999996 | 5.31 | 6.29 | 7.3 | 8.32 | 9.32 | 10.37 | 11.39 | 12.4
Cl SD2030 | -0.391 | -0.319 | -0.25 | -0.166 | -0.072 | 0.006 | 0.105 | 0.267 | 0.438 | 0.557 | 0.659 | 0.736 | 0.804 | 0.879 | 0.958 | 1.015 | 1.06 | 1.08 | 0.999
Cd SD2030 | 0.0523 | 0.0315 | 0.0236 | 0.0187 | 0.0154 | 0.0141 | 0.0148 | 0.0165 | 0.0157 | 0.0146 | 0.0137 | 0.0157 | 0.0193 | 0.0228 | 0.0269 | 0.0334 | 0.0443 | 0.0709 | 0.1818
Chart: AoA (deg)
| -5.95 | -4.96 | -3.96 | -2.94 | -1.92 | -0.87 | 0.1 | 1.21 | 2.1800000000000002 | 3.25 | 4.2699999999999996 | 5.31 | 6.29 | 7.3 | 8.32 | 9.32 | 10.37 | 11.39 | 12.4
SD2030 | -7.4761 | -10.127 | -10.5932 | -8.877 | -4.6753 | 0.42553 | 7.0946 | 16.1818 | 27.8981 | 38.1507 | 48.1022 | 46.879 | 41.658 | 38.5526 | 35.6134 | 30.3892 | 23.9278 | 15.2327 | 5.495

## Slide 7: Model Design Process
PropID used to optimize chord and twist of all stations for axial induction = 0.342 at 4deg AoA with Rho = 1000 (kg/m^3).
  Axial induction increased 2.59% to attain accurate thrust scaling in fresh water.
  Re# = 100k test data
  Diameter and RPM Froude scaled.
  Full Scale reference rotor: 45.5m 30% Thick Estimate ‘Hydro Loop2’
Chart: Chord Distribution
| 0.14929999999999999 | 0.44779999999999998 | 0.74639999999999995 | 1.0449999999999999 | 1.3434999999999999 | 1.6420999999999999 | 1.9406000000000001 | 2.2391999999999999 | 2.5377999999999998 | 2.8363 | 2.9855999999999998
Current | 0.53913 | 0.97406 | 0.72322 | 0.55437 | 0.44459 | 0.36907 | 0.31336 | 0.26744 | 0.21934 | 0.13915 | 0.09905
Chart: Twist + Pitch Distribution
| 0.14929999999999999 | 0.44779999999999998 | 0.74639999999999995 | 1.0449999999999999 | 1.3434999999999999 | 1.6420999999999999 | 1.9406000000000001 | 2.2391999999999999 | 2.5377999999999998 | 2.8363 | 2.9855999999999998
Current | 10.161 | 23.3004 | 14.9297 | 10.4679 | 7.7797 | 6.0022 | 4.7454 | 3.812 | 3.0923 | 2.5208 | 2.2351

## Slide 8: Model Rotor Hydrodynamics
Chart: Lift Coefficient Distribution
| 0.05 | 0.15 | 0.25 | 0.35 | 0.45 | 0.55000000000000004 | 0.65 | 0.75 | 0.85 | 0.95
Current | 0.8072 | 0.632 | 0.632 | 0.632 | 0.632 | 0.632 | 0.632 | 0.632 | 0.632 | 0.632
Chart: Axial Induction Factor Distribution
| 0.05 | 0.15 | 0.25 | 0.35 | 0.45 | 0.55000000000000004 | 0.65 | 0.75 | 0.85 | 0.95
Current | 0.1883 | 0.342 | 0.342 | 0.342 | 0.342 | 0.342 | 0.342 | 0.342 | 0.342 | 0.342
Chart: Reynolds Number Distribution - SeaWater
| 0.05 | 0.15 | 0.25 | 0.35 | 0.45 | 0.55000000000000004 | 0.65 | 0.75 | 0.85 | 0.95
Current | 58038.1902 | 153221.4471 | 165472.9121 | 169567.1517 | 171286.1072 | 171942.4357 | 171442.3759 | 168160.7335 | 155878.0147 | 110310.0658
Axial Induction: 0.342
Re#: 168k
Design Cl: 0.65

## Slide 9: Performance Comparison
Similar performance at design point:
  Model Cp: 0.428
  Full scale Cp: 0.425
Chart: Full-Scale Lift-to-Drag Ratio Distribution
| 0.05 | 0.15 | 0.25 | 0.35 | 0.45 | 0.55000000000000004 | 0.65 | 0.75 | 0.85 | 0.95
Current | 1.5222 | 38.0634 | 38.0634 | 38.0634 | 38.0634 | 38.0634 | 38.0634 | 55.7216 | 59.396 | 64.5775
Chart: Model Lift-to-Drag Ratio Distribution
| 0.05 | 0.15 | 0.25 | 0.35 | 0.45 | 0.55000000000000004 | 0.65 | 0.75 | 0.85 | 0.95
Current | 1.1635 | 44.3051 | 44.3052 | 44.305 | 44.3052 | 44.3052 | 44.3052 | 44.3052 | 44.3052 | 44.3052

## Slide 10: Reynolds Number Calibration
Airfoil A = 100k Re#
Airfoil B = 200k Re#
Blended Airfoil = 168k Re#
Chart: Lift Coeff.
| -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Airfoil A | -0.32191 | -0.25276 | -0.17094 | -0.079373 | -0.0036571 | 0.094794 | 0.23635 | 0.40627 | 0.5292 | 0.632 | 0.71305 | 0.78388 | 0.85672 | 0.93322 | 0.99676 | 1.0441 | 1.0724 | 1.0311
Airfoil B | -0.3546 | -0.25596 | -0.14565 | 0.00015686 | 0.1408 | 0.24331 | 0.3203 | 0.41826 | 0.5121 | 0.60853 | 0.70519 | 0.79766 | 0.88938 | 0.97327 | 1.0418 | 1.0918 | 1.1309 | 1.0979
Blended airfoil | -0.34414 | -0.25494 | -0.15374 | -0.025293 | 0.094574 | 0.19578 | 0.29343 | 0.41442 | 0.51757 | 0.61604 | 0.70771 | 0.79325 | 0.87893 | 0.96046 | 1.0274 | 1.0765 | 1.1121 | 1.0765
Chart: Drag Coeff.
| -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Airfoil A | 0.032808 | 0.02432 | 0.019294 | 0.015314 | 0.014124 | 0.014897 | 0.016622 | 0.016186 | 0.015234 | 0.014265 | 0.015404 | 0.018112 | 0.021812 | 0.025745 | 0.03108 | 0.040124 | 0.060676 | 0.13804
Airfoil B | 0.03101 | 0.01944 | 0.016176 | 0.014157 | 0.011371 | 0.011 | 0.011811 | 0.012814 | 0.013766 | 0.014735 | 0.015702 | 0.016704 | 0.018406 | 0.021059 | 0.02676 | 0.03159 | 0.038559 | 0.12172
Blended airfoil | 0.031585 | 0.021002 | 0.017174 | 0.014527 | 0.012252 | 0.012247 | 0.01335 | 0.013893 | 0.014236 | 0.014585 | 0.015607 | 0.017155 | 0.019496 | 0.022558 | 0.028142 | 0.034321 | 0.045636 | 0.12694

## Slide 11: Design Point (TSR = 8) Comparisons
Rotor thrust scales very well at the design TSR
  0.6% difference – well within test accuracy.
Rotor Torque: 2.7% difference
Root Bending Moment: 3.1% difference
Chart: Froude Scaled Rotor Speed (RPM)
| 1.679 | 3.3580000000000001 | 5.0369999999999999 | 6.7160000000000002 | 8.3949999999999996 | 10.074 | 11.753 | 13.432 | 15.111000000000001 | 16.79 | 18.469000000000001 | 20.148 | 21.827000000000002 | 23.506 | 25.184999999999999 | 26.864000000000001 | 28.542999999999999 | 30.222000000000001 | 31.901 | 33.58 | 35.259 | 36.938000000000002 | 38.616999999999997 | 40.295999999999999 | 41.975000000000001
Froude Scaled 45.5m Data | 0.00012285 | 0.00049142 | 0.0011057 | 0.0019657 | 0.0030714 | 0.0044228 | 0.0060199 | 0.0078627 | 0.0099513 | 0.012286 | 0.014866 | 0.017691 | 0.020763 | 0.02408 | 0.027642 | 0.031451 | 0.035505 | 0.039805 | 0.044351 | 0.049142 | 0.054179 | 0.059462 | 0.064991 | 0.070765 | 0.076785
Model Data | 0.000119 | 0.000476 | 0.001072 | 0.001905 | 0.002977 | 0.004287 | 0.005835 | 0.007621 | 0.009645 | 0.011908 | 0.014409 | 0.017147 | 0.020124 | 0.023339 | 0.026793 | 0.030484 | 0.034414 | 0.038582 | 0.042987 | 0.047632 | 0.052514 | 0.057634 | 0.062993 | 0.068589 | 0.074424
Chart: Froude Scaled Rotor Speed (RPM)
| 1.679 | 3.3580000000000001 | 5.0369999999999999 | 6.7160000000000002 | 8.3949999999999996 | 10.074 | 11.753 | 13.432 | 15.111000000000001 | 16.79 | 18.469000000000001 | 20.148 | 21.827000000000002 | 23.506 | 25.184999999999999 | 26.864000000000001 | 28.542999999999999 | 30.222000000000001 | 31.901 | 33.58 | 35.259 | 36.938000000000002 | 38.616999999999997 | 40.295999999999999 | 41.975000000000001
Froude Scaled 45.5m Data | 0.00041171 | 0.0016468 | 0.0037055 | 0.0065875 | 0.010293 | 0.014822 | 0.020174 | 0.02635 | 0.033349 | 0.041172 | 0.049818 | 0.059287 | 0.06958 | 0.080697 | 0.092637 | 0.1054 | 0.11899 | 0.1334 | 0.14863 | 0.16469 | 0.18157 | 0.19927 | 0.2178 | 0.23715 | 0.25732
Model Data | 0.000409 | 0.001636 | 0.003682 | 0.006545 | 0.010227 | 0.014726 | 0.020044 | 0.02618 | 0.033135 | 0.040907 | 0.049497 | 0.058906 | 0.069133 | 0.080177 | 0.09204 | 0.10472 | 0.11822 | 0.13254 | 0.14767 | 0.16363 | 0.1804 | 0.19799 | 0.2164 | 0.23562 | 0.25567
Chart: Froude Scaled Rotor Speed (RPM)
| 1.679 | 3.3580000000000001 | 5.0369999999999999 | 6.7160000000000002 | 8.3949999999999996 | 10.074 | 11.753 | 13.432 | 15.111000000000001 | 16.79 | 18.469000000000001 | 20.148 | 21.827000000000002 | 23.506 | 25.184999999999999 | 26.864000000000001 | 28.542999999999999 | 30.222000000000001 | 31.901 | 33.58 | 35.259 | 36.938000000000002 | 38.616999999999997 | 40.295999999999999 | 41.975000000000001
Froude Scaled 45.5m Data | 2.486e-05 | 9.9443e-05 | 0.00022375 | 0.00039778 | 0.00062152 | 0.00089499 | 0.0012182 | 0.0015911 | 0.0020137 | 0.0024861 | 0.0030082 | 0.00358 | 0.0042015 | 0.0048727 | 0.0055937 | 0.0063644 | 0.0071848 | 0.0080549 | 0.0089748 | 0.0099444 | 0.010964 | 0.012033 | 0.013151 | 0.01432 | 0.015538
Model Data | 2.4e-05 | 9.7e-05 | 0.000218 | 0.000387 | 0.000605 | 0.000871 | 0.001186 | 0.001549 | 0.00196 | 0.00242 | 0.002928 | 0.003485 | 0.00409 | 0.004743 | 0.005445 | 0.006195 | 0.006993 | 0.00784 | 0.008736 | 0.009679 | 0.010672 | 0.011712 | 0.012801 | 0.013938 | 0.015124

## Slide 12: Off-Design Comparisons (1.9m/s)
Chart: TSR
| 16.000026664977696 | 15.578973331688811 | 15.157919998399926 | 14.736866665111036 | 14.315813331822152 | 13.894759998533264 | 13.473706665244377 | 13.052653331955488 | 12.631599998666601 | 12.210546665377716 | 11.78949333208883 | 11.368439998799941 | 10.947386665511058 | 10.526333332222169 | 10.105279998933282 | 9.6842266656443936 | 9.2631733323555103 | 8.8421199990666235 | 8.4210666657777349 | 8.0000133324888481 | 7.578959999199963 | 7.1579066659110762 | 6.7368533326221884 | 6.3157999993333007 | 5.8947466660444148 | 5.4736933327555288 | 5.0526399994666411 | 4.6315866661777552 | 4.2105333328888674 | 3.7894799995999815 | 3.3684266663110942 | 2.9473733330222074 | 2.5263199997333206 | 2.1052666664444337 | 1.6842133331555471 | 1.2631599998666603 | 0.84210666657777355
Froude Scaled 45.5m Data | 0.23392 | 0.22971 | 0.2255 | 0.22127 | 0.21705 | 0.21281 | 0.20853 | 0.20426 | 0.19996 | 0.19567 | 0.19135 | 0.187 | 0.18259 | 0.17816 | 0.17373 | 0.16932 | 0.16488 | 0.1603 | 0.15538 | 0.15009 | 0.14402 | 0.13754 | 0.13077 | 0.12372 | 0.11631 | 0.10837 | 0.099762 | 0.088975 | 0.07655 | 0.063371 | 0.049821 | 0.037776 | 0.028216 | 0.020991 | 0.015982 | 0.012739 | 0.010824
Model Data | 0.1737 | 0.17337 | 0.17238 | 0.17189 | 0.17131 | 0.17063 | 0.16986 | 0.16909 | 0.16825 | 0.1674 | 0.16656 | 0.16565 | 0.16465 | 0.16346 | 0.162 | 0.16016 | 0.15801 | 0.15551 | 0.15262 | 0.14938 | 0.14556 | 0.14132 | 0.13655 | 0.13146 | 0.12577 | 0.11835 | 0.10551 | 0.090781 | 0.075853 | 0.061547 | 0.049472 | 0.039904 | 0.032671 | 0.027287 | 0.023209 | 0.020265 | 0.018274
Chart: TSR
| 16.000026664977696 | 15.578973331688811 | 15.157919998399926 | 14.736866665111036 | 14.315813331822152 | 13.894759998533264 | 13.473706665244377 | 13.052653331955488 | 12.631599998666601 | 12.210546665377716 | 11.78949333208883 | 11.368439998799941 | 10.947386665511058 | 10.526333332222169 | 10.105279998933282 | 9.6842266656443936 | 9.2631733323555103 | 8.8421199990666235 | 8.4210666657777349 | 8.0000133324888481 | 7.578959999199963 | 7.1579066659110762 | 6.7368533326221884 | 6.3157999993333007 | 5.8947466660444148 | 5.4736933327555288 | 5.0526399994666411 | 4.6315866661777552 | 4.2105333328888674 | 3.7894799995999815 | 3.3684266663110942 | 2.9473733330222074 | 2.5263199997333206 | 2.1052666664444337 | 1.6842133331555471 | 1.2631599998666603 | 0.84210666657777355
Froude Scaled 45.5m Data | -0.00085431 | -0.00038073 | 9.4725e-05 | 0.00057106 | 0.0010502 | 0.0015269 | 0.0020021 | 0.0024819 | 0.0029642 | 0.0034526 | 0.0039503 | 0.0044619 | 0.0049883 | 0.0055345 | 0.006099 | 0.0066898 | 0.0073091 | 0.007942 | 0.0085736 | 0.0091976 | 0.0097556 | 0.010282 | 0.010784 | 0.011265 | 0.011717 | 0.012115 | 0.012437 | 0.012439 | 0.011937 | 0.010919 | 0.0093017 | 0.0074546 | 0.0056289 | 0.0039889 | 0.0026584 | 0.001648 | 0.00093304
Model Data | -0.001533 | -0.001018 | -0.00052 | -1.7e-05 | 0.00048 | 0.000975 | 0.001471 | 0.001972 | 0.002477 | 0.002993 | 0.003521 | 0.004062 | 0.00462 | 0.005194 | 0.005791 | 0.006409 | 0.007038 | 0.007672 | 0.008312 | 0.008955 | 0.009573 | 0.010188 | 0.010777 | 0.011351 | 0.011873 | 0.012083 | 0.011187 | 0.009496 | 0.00756 | 0.005505 | 0.00444 | 0.003481 | 0.00269 | 0.002064 | 0.001565 | 0.001184 | 0.000914
Chart: TSR
| 16.000026664977696 | 15.578973331688811 | 15.157919998399926 | 14.736866665111036 | 14.315813331822152 | 13.894759998533264 | 13.473706665244377 | 13.052653331955488 | 12.631599998666601 | 12.210546665377716 | 11.78949333208883 | 11.368439998799941 | 10.947386665511058 | 10.526333332222169 | 10.105279998933282 | 9.6842266656443936 | 9.2631733323555103 | 8.8421199990666235 | 8.4210666657777349 | 8.0000133324888481 | 7.578959999199963 | 7.1579066659110762 | 6.7368533326221884 | 6.3157999993333007 | 5.8947466660444148 | 5.4736933327555288 | 5.0526399994666411 | 4.6315866661777552 | 4.2105333328888674 | 3.7894799995999815 | 3.3684266663110942 | 2.9473733330222074 | 2.5263199997333206 | 2.1052666664444337 | 1.6842133331555471 | 1.2631599998666603 | 0.84210666657777355
Froude Scaled 45.5m Data | 0.074926 | 0.073329 | 0.071734 | 0.070141 | 0.068556 | 0.066968 | 0.065379 | 0.063797 | 0.062218 | 0.060644 | 0.059073 | 0.057504 | 0.055937 | 0.054378 | 0.052825 | 0.051288 | 0.049762 | 0.048194 | 0.046531 | 0.04476 | 0.042755 | 0.040639 | 0.038442 | 0.036184 | 0.033853 | 0.031412 | 0.028839 | 0.025889 | 0.022529 | 0.018834 | 0.014789 | 0.011046 | 0.0080203 | 0.005702 | 0.0040881 | 0.0030479 | 0.0024297
Model Data | 0.055678 | 0.055231 | 0.054749 | 0.054308 | 0.053845 | 0.053355 | 0.052844 | 0.05235 | 0.051843 | 0.051346 | 0.05085 | 0.050327 | 0.049759 | 0.049136 | 0.048432 | 0.047635 | 0.046754 | 0.045758 | 0.044652 | 0.043446 | 0.042065 | 0.040573 | 0.038921 | 0.037186 | 0.035314 | 0.033093 | 0.02993 | 0.026027 | 0.021707 | 0.017306 | 0.013489 | 0.010431 | 0.008128 | 0.006444 | 0.005162 | 0.004246 | 0.00362
TSR=6 is minimum computed with test data.
    Lower values use Viterna flat-plate approximation.
  Thrust diverges from scaled values at TSR above design point.
  Only test cases that experience TSR above 8.0 are hydraulic failures.
Differences in off-design performance result from hydrofoil, Re#, and AoA differences.
  See next slide and previous hydrofoil polar data plots.
May be able to adjust blade pitch or TSR to improve thrust accuracy for off-design cases based on results of captured test.

## Slide 13: Blade Element Data
Difference in Cl drives discrepancy in high-TSR axial induction and rotor thrust.
Chart: Thrust Coefficient
| 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Full Scale TSR=8 | 0.877 | 0.867 | 0.858 | 0.849 | 0.837 | 0.82 | 0.748 | 0.528
Model TSR=8 | 0.893 | 0.885 | 0.877 | 0.864 | 0.855 | 0.83 | 0.759 | 0.526
Full Scale TSR=16 | 0.763 | 0.938 | 1.066 | 1.216 | 1.366 | 1.571 | 1.364 | 1.224
Model TSR=16 | 0.439 | 0.634 | 0.801 | 0.918 | 1 | 1.08 | 1.132 | 0.972
Chart: Axial Induction
| 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Full Scale TSR=8 | 0.33 | 0.322 | 0.316 | 0.312 | 0.309 | 0.31 | 0.311 | 0.318
Model TSR=8 | 0.342 | 0.335 | 0.33 | 0.322 | 0.321 | 0.319 | 0.319 | 0.319
Full Scale TSR=16 | 0.26 | 0.383 | 0.516 | 0.63 | 0.721 | 0.826 | 0.719 | 0.667
Model TSR=16 | 0.127 | 0.2 | 0.28 | 0.363 | 0.453 | 0.528 | 0.572 | 0.535
Chart: Torque Coefficient
| 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Full Scale TSR=8 | 0.271 | 0.193 | 0.147 | 0.117 | 0.095 | 0.084 | 0.067 | 0.042
Model TSR=8 | 0.273 | 0.196 | 0.15 | 0.12 | 0.098 | 0.08 | 0.063 | 0.038
Full Scale TSR=16 | 0.085 | 0.045 | 0.012 | -0.01 | -0.026 | -0.024 | -0.01 | 0.001
Model TSR=16 | 0.03 | 0.024 | 0.013 | -0.001 | -0.015 | -0.024 | -0.028 | -0.017
Chart: Induced Flow Velocity Angle
| 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Full Scale TSR=8 | 18.55 | 13.97 | 11.16 | 9.28 | 7.93 | 6.55 | 6.07 | 5.39
Model TSR=8 | 18.17 | 13.68 | 10.93 | 9.13 | 7.78 | 6.78 | 6.01 | 5.38
Full Scale TSR=16 | 10.41 | 6.27 | 3.84 | 2.41 | 1.54 | 0.83 | 1.18 | 1.26
Model TSR=16 | 12.26 | 8.11 | 5.7 | 4.13 | 3.01 | 2.25 | 1.81 | 1.75

## Slide 14: Additional Analysis
Cavitation Check
  Min. Cavitation Number: 4.7
    TSR=14.5, Flow Speed: 0.5m/s, Hub Depth: 2m
  Cpmin estimated to be ~ -4.0 at Clmax
    verify with Xfoil analysis
Off-Design TSR
  Viterna flat-plate post-stall
  Start-up Torque w/o pitch control
Chart: AoA (deg)
| -180 | -170 | -160 | -150 | -140 | -130 | -120 | -110 | -100 | -90 | -80 | -70 | -60 | -50 | -40 | -30 | -20 | -10 | -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180
CL | 0 | 0.62796 | 0.59429 | 0.54905 | 0.52353 | 0.47601 | 0.39499 | 0.28175 | 0.14539 | -5.0664e-17 | -0.14539 | -0.28175 | -0.39499 | -0.47601 | -0.52353 | -0.54905 | -0.59429 | -0.60708 | -0.34414 | -0.25494 | -0.15374 | -0.025293 | 0.094574 | 0.19578 | 0.29343 | 0.41442 | 0.51757 | 0.61604 | 0.70771 | 0.79325 | 0.87893 | 0.96046 | 1.0274 | 1.0765 | 1.1121 | 1.0765 | 0.84899 | 0.78436 | 0.7479 | 0.68002 | 0.56427 | 0.40251 | 0.2077 | 7.2377e-17 | -0.14539 | -0.28175 | -0.39499 | -0.47601 | -0.52353 | -0.54905 | -0.59429 | -0.62796 | 0
CD | 0.077544 | 0.11201 | 0.21114 | 0.36266 | 0.54778 | 0.74347 | 0.92527 | 1.0703 | 1.1598 | 1.182 | 1.1598 | 1.0703 | 0.92527 | 0.74347 | 0.54778 | 0.36266 | 0.21114 | 0.099699 | 0.031585 | 0.021002 | 0.017174 | 0.014527 | 0.012252 | 0.012247 | 0.01335 | 0.013893 | 0.014236 | 0.014585 | 0.015607 | 0.017155 | 0.019496 | 0.022558 | 0.028142 | 0.034321 | 0.045636 | 0.12694 | 0.21114 | 0.36266 | 0.54778 | 0.74347 | 0.92527 | 1.0703 | 1.1598 | 1.182 | 1.1598 | 1.0703 | 0.92527 | 0.74347 | 0.54778 | 0.36266 | 0.21114 | 0.11201 | 0.077544
Viterna Flat-Plate Post-Stall Estimation

## Slide 15: Scaled Blade Design
Model Blade Design Requirements:
Pitch adjustability of +-0.5deg.
Trailing edge thickness of ~0.1mm.
Ability to operate in submerged environment.
Mass and CG to be evaluated for inertial match.

## Slide 16: Scaled Blade Design
Extreme Loads Design Point
TSR 8.000
Rotor Speed 41.975 RPM
Flow Speed 0.500 m/s
Pitch -1.504 deg
Diameter 1.820 m
# | r/R | Relm (m) | Twist (deg) | Chord (m) | Relative Thickness (t/c %) | Absolute Thickness (m) | Thr/Len (N/m) | Trq/Len (N)
 |  | 0 |  | 0 | 100% | 0.092 |  | 
1 | 0.050 | 0.046 | 23.553 | 0.092 | 100.00% | 0.092 | 9.1 | 0.365
2 | 0.150 | 0.137 | 23.553 | 0.155 | 40.00% | 0.062 | 37.5 | 2.784
3 | 0.250 | 0.228 | 15.078 | 0.218 | 8.56% | 0.0186608 | 79.3 | 5.23
4 | 0.350 | 0.319 | 10.558 | 0.167 | 8.56% | 0.0142952 | 111.0 | 7.286
5 | 0.450 | 0.41 | 7.833 | 0.134 | 8.56% | 0.0114704 | 142.7 | 9.173
6 | 0.550 | 0.501 | 6.032 | 0.111 | 8.56% | 0.0095016 | 174.1 | 10.904
7 | 0.650 | 0.592 | 4.758 | 0.094 | 8.56% | 0.0080464 | 204.4 | 12.438
8 | 0.750 | 0.683 | 3.812 | 0.08 | 8.56% | 0.006848 | 230.6 | 13.608
9 | 0.850 | 0.774 | 3.083 | 0.066 | 8.56% | 0.0056496 | 242.7 | 13.763
10 | 0.950 | 0.865 | 2.503 | 0.042 | 8.56% | 0.0035952 | 192.1 | 10.44

## Slide 17: Scaled Blade Design

## Slide 18: Scaled Blade Design – Proposed Structure
Rapid Prototyping with Watershed XC11122
ABS-Like Properties
2650 MPa Tensile Modulus
47.1 MPa min Tensile Strength (ASTM D638)
Max root moment of 76 N-m
Very thin airfoil for hydrodynamic scaling 8.56%
Initial calculations show ABS-type material is feasible
Working with rapid prototype company to assess manufacturing feasibility and costs.

## Slide 19: Scaled Blade Design – Proposed Structure
Basic structural analysis performed for strain analysis
Assumes no twist in calculation
Assumes principal axes of airfoil are aligned with chord line.
Material safety factor of 1.35
Tip deflection calculation pending
Detailed 3D model pending

## Slide 20: Scaled Blade Design – Pitch Adjustment
Considerations for adjustable pitch
Easy manual adjustment of pitch +-2deg with intervals of +-.5deg desired
Sleeve connection of root envisioned with 9 tapered axial holes for insertion of alignment pins.
Next Steps
Define manufacturing plan
Detailed 3D sectional stress analysis
Root connection and pitch adjustment design

## Slide 21: Next Steps
Resolve high-TSR thrust discrepancy
3D Effects
Rotational Inertia
Root Attachment
  Pitch adjustment
Loft