## Slide 1: Initial FE Model
Single blade modeled
  Full scale
  Elements: 79,200
    76,800 brick elements (C3D8I)
    2,400 wedge elements (C3D6)
Composite material parameters
Elements for structural plies with outer surface material orientations
  Elements for core plies with mid-surface material orientations
  Smeared material properties used (estimated):
All tang exterior nodes fixed

## Slide 2: Initial FEA: single full scale blade, “steady” CFD analysis

## Slide 3: Interpolated FE data
 | Steady – Speed (m/s) |  |  |  |  |  | 3 m/s unsteady – time step |  |  | 2.0 and 2.6 unsteady | 
 | 2 | 2.2 | 2.4 | 2.6 | 2.8 | 3 | 3856 | 3870 | 3876 | 3146 | 4950
Fx | -2,679 | -3,073 | -3,469 | -3,876 | -4,273 | -4,666 | -5,550 | -5,538 | -5,526 | -3,298 | -4,671
Fy | 108 | 129 | 154 | 181 | 212 | 247 | 404 | 406 | 404 | 174 | 300
Fz | 484 | 623 | 784 | 961 | 1,162 | 1,382 | 1,969 | 1,979 | 1,983 | 704 | 1,401
Ftotal | 2,724 | 3,138 | 3,560 | 3,998 | 4,433 | 4,873 | 5,903 | 5,895 | 5,885 | 3,377 | 4,885
Mx | -27,892 | -35,985 | -45,222 | -55,436 | -66,882 | -79,381 | -112,620 | -113,125 | -113,310 | -41,116 | -80,893
My | -6,768 | -7,132 | -7,439 | -7,740 | -7,939 | -8,070 | -8,056 | -8,027 | -7,998 | -7,446 | -7,988
Mz | -177,679 | -202,637 | -227,558 | -253,018 | -277,543 | -301,607 | -354,857 | -354,174 | -353,322 | -218,404 | -302,941
Mtotal | 179,982 | 205,931 | 232,127 | 259,136 | 285,598 | 311,982 | 372,386 | 371,889 | 371,133 | 222,366 | 313,657
max disp | 2.783 | 3.153 | 3.523 | 3.903 | 4.268 | 4.624 | 5.433 | 5.425 | 5.411 | 3.448 | 4.697
max strain* | 1,593 | 1,798 | 2,001 | 2,208 | 2,405 | 2,595 | 3,017 | 3,011 | 3,002 | 1,968 | 2,638
min strain* | -1,800 | -2,034 | -2,268 | -2,506 | -2,734 | -2,955 | -3,452 | -3,446 | -3,436 | -2,230 | -3,007
*away from root
TDC

## Slide 4: 1-piece rotor assembly
Fairing (GRP)
Tail cone (GRP)
Hub with tapered bore
Bracket
Main shaft

## Slide 5
Current design
1-piece rotor

## Slide 6: Rotor FE Model Assembly
Screws used to attach bracket to hub
  Socket head cap screws, 1 inch diameter by 3 inches long
  Screw head tied to bracket
  Screw threads tied to hub
  Preload force of 15,000 lbs. per screw specified in first step
    Typical value for Grade 2 screws (stainless hardware)
Clearance specified between bracket and hub to preload the rotor
  Set at 0.015 inch
Radial clearance between:
  hub tube and rotor bore: 0.02 inch
  Hub tube and bracket bore: 0.01 inch
Loading on rotor:
  1 blade at TDC pressures, 2 blades at BDC pressures
  2 blades at TDC pressures, 1 blade at BDC pressures
Hub tube inner surface fully restrained
All friction coefficients: 0.15
2.6 m/s unsteady pressures applied to blade
Materials:
  Ductile iron
  Steel
  Rubber (E = 2.5 ksi, lower bound, nu = 0.48)
  Composite material (measured):
Clearance: 0.015 inch
Blade contact with these raised surfaces

## Slide 7: Rotor FE Model Assembly
Blade contact with these raised surfaces
Tied contact
Bracket contact with hub at screw locations
Blade contact with bracket and hub raised surfaces
Blade contact with LE rubber
  Erubber = 2.5 ksi
    Lower bound
  nurubber = 0.48
Hub pocket contact with LE rubber
Blade bore contact with hub tube
  Line-to-line fit
Bracket bore contact with hub tube
  0.01 inch radial clearance
Bracket contact with end face of LE rubber
All friction coefficients = 0.15
Hub bore fully restrained
2.6 m/s unsteady pressures applied to blade

## Slide 8: Principal strains in rotor
Pressure side
Suction side
Suction side
Pressure side
Max principal
Min principal
3,570 με

## Slide 9: Stresses in hub and bracket