## Slide 1: Half scale blade test concept
9/12/16

## Slide 2: Half scale blade testing
Aluminum plate, 2 inches thick
Steel blocks

## Slide 3: Blade clamping
1/8 inch thick rubber sheet
Install shims after determining suitable preload
1 inch socket head screws

## Slide 4: Vertical distances from table surface
0
36
6.0
29
Bottom surface of load cell positioned at 29 inches above table surface
Bottom surface of adapter is 6 inches above table surface
Gap between top of adapter and bottom of load cell indicates that the spacing is sufficient

## Slide 5
11.04
From this plane to this edge

## Slide 6
11.04

## Slide 7: Test machine displacement/force
With clamp located as shown in previous figures,
  displacement at load patch location for TDC point loading: 0.862 inch
  displacement at load patch location for BDC point loading: 0.558 inch
Test displacement: 0.71 ± 0.152 inch
With load applied at load location shown in previous figures,
  Load for TDC: 689 lbs.
  Load for BDC: 445 lbs.
Test load: 567 ± 122 lbs.

## Slide 8: Alternate clamps required for Gen5d blade versus untwisted blade
Nominal blade setup
Untwisted blade setup
Make 2 sets of blocks for testing either…

## Slide 9: Drawings required:
(1) Machined part, Aluminum plate, 2 inches thick
(4) Machined steel blocks
(2) Machined steel blocks
Drawings:
7 Machined parts
1 Assembly
Test machine (existing)
Actuator assembly (existing)
Half-scale rotor (existing)
Pipe and pipe flanges (purchased)

## Slide 10: Assembly
Show 2 test setups
  Single blade and its steel blocks and rubber sheets
  3-blade rotor and its blocks and rubber sheets
  (note, smaller blocks at loading location do not change)
Single blade test setup
3blade rotor test setup

## Slide 11: Changed to using nuts on 1 inch screws

## Slide 12: Purchased parts
Qty: 2
Qty: 1

## Slide 13
Alum plate: 33.25 x 17 x 2
Steel blocks: 2: 4 x 3 x 17, 2: 4 x 4 x 17
Steel blocks: 2: 2.75 x 2.75 x 1.375
Rubber sheet: .125 thick